## Slide 1: Apollo Robotics MES Server Socket Communication Rule

## Slide 2: MES Socket Communication Rule
Command | Content | Reference
S | Material input (Track In) | Char
E | Work done(Track Out) | Char
C | Communication Check | Char
STX | Start Of Text (HEX : 2) | ASC
EXT | End Of Text (HEX : 3) | ASC
ACK | OK (HEX : 6) | ASC
NAK | NG (HEX : F) | ASC
/ | Sortation | Char
* For Equipments without Recipe ID, please enter data such as Model ID
Track In | STX/S/(Code)/(Model ID)/(Recipe ID)/(Machine ID)/ETX
Ack : Track In OK | STX/S/ACK/ETX
Ack : Track In NG | STX/S/NAK/(Code) : (Error Message)/ETX
Track Out | STX/E/(Code)/(Model ID)/(Recipe ID)/(Machine ID)/ETX
Ack : Track Out OK | STX/E/ACK/ETX
Ack : Track Out NG | STX/E/NAK/(Code) : (Error Message)/ETX
Com Check | STX/C/ETX
Com Ack | STX/C/ETX

## Slide 3: Track In (Normal)
Server
Client
STX/S/(Code)/(Model ID)/(Recipe ID)/(Machine ID)/ETX
STX/S/ACK/ETX
Working

## Slide 4: Track In (Error)
Server
Client
STX/S/(Code)/(Model ID)/(Recipe ID)/(Machine ID)/ETX
STX/S/NAK/(Code : Error Message)/ETX
Popup Error Message – Not Working

## Slide 5: Track Out (Normal)
Server
Client
STX/E/(Code)/(Model ID)/(Recipe ID)/(Machine ID)/ETX
STX/E/ACK/ETX
Working

## Slide 6: Track Out (Error)
Server
Client
STX/E/(Code)/(Model ID)/(Recipe ID)/(Machine ID)/ETX
STX/E/NAK/(Code : Error Message)/ETX
Popup Error Message – Not Working

## Slide 7: Com Check
Server
Client
STX/C/ETX
STX/C/ETX
Disconnect from the client and generate an error
pop-up if the server does not respond